## Slide 1: Multi-Finger Gestural Interaction with 3D Volumetric Displays
Tovi Grossman
Daniel Wigdor
Ravin Balakrishnan
Presented at UIST2004, Santa Fe, NM, USA

## Slide 2: Volumetric Displays
Points illuminated in true 3D
360° viewing angle
Available commercially

## Slide 3: Volumetric Displays

## Slide 4: Current Use
Non-interactive output-only

## Slide 5: Motivation
Understand surrounding issues
Develop appropriate interaction techniques
  Menus and widgets
  Object Selection
  Transformations

## Slide 6: Previous Work
Balakrishnan, Fitzmaurice, Kurtenbach (2001)
  Discusses possible interaction scenarios
  Mock-up prototypes
Balakrishnan, Fitzmaurice, & Kurtenbach. IEEE Computer 2001

## Slide 7: Previous Work
Balakrishnan et al (2001)
  Discusses possible interaction scenarios
  Mock-up prototypes
Much VR Research
  3D Selection
  3D Object Manipulation
  3D Widgets

## Slide 8: Unique Issues
Objects within arm’s reach
Objects inside enclosure
Direct link between input and display

## Slide 9: Design Principles
Volumetric Display as exclusive platform

## Slide 10: Design Principles
Multi-Viewpoint Operation
Out-of-Viewpoint Operation
Direct Touch and Gestural Input

## Slide 12: Implementation - Display
Perspecta Spatial 3D System
  10" spherical image
  198 2D slices, 768x768 each
  24Hz refresh rate

## Slide 13: Implementation – Finger Tracking
Vicon motion tracking system
  5 Cameras
Tracked 5mm markers
  Real Time, 120Hz, sub mm precision

## Slide 14: Implementation – Finger Tracking
Detect away, hover, and touch

## Slide 15: Command Input
Surface Menus
  On outside surface of display
  Tap to enter command
  Hold to maintain mode

## Slide 16: Command Input
Postures and Gestures
  Point

## Slide 17: Command Input
Postures and Gestures
  Point
  Flat

## Slide 18: Command Input
Postures and Gestures
  Point
  Flat
  Pinch

## Slide 19: Command Input
Postures and Gestures
  Point
  Flat
  Pinch
  Curl

## Slide 20: Command Input
Postures and Gestures
  Point
  Flat
  Pinch
  Curl
  Trigger

## Slide 21: Command Input
Postures and Gestures
  Point
  Flat
  Pinch
  Curl
  Trigger
  Scrub

## Slide 22: Interaction Techniques
Surface Browser
  Used for object previews, organization
    File browser

## Slide 23: Surface Browser

## Slide 24: Interaction Techniques
Transformations
  Widgets for visual feedback
    Colour to indicate active
Rotate | Translate | Scale
touch & drag | pinch & scrub | bimanual drag

## Slide 25: Transformations

## Slide 26: Interaction Techniques
Constrained Transformations

## Slide 27: Interaction Techniques
Adding Models
  Surface browser allows maintained context

## Slide 28: Interaction Techniques
Selection: Ray cursor with depth control

## Slide 29: Interaction Techniques
Object Snapping
  Menu activated
  Objects snap to faces, edges

## Slide 30: Object Snapping

## Slide 31: Contributions
Identified issues unique to domain
  True 3D
  Enclosed Space
  Within-reach
Provided generalizable techniques
  Menus and widgets
  Object Selection
  Transformations
Implementation

## Slide 32: Acknowledgements
Actuality Systems
DGP Lab and members
John Hancock

## Slide 33: Questions?